## Slide 1: Smart Car Parking System
Automated Detection with Button Confirmation and Time-Limit Alert
PATRICK Twinamatsiko | VU-BSF-2311-0581-WEE
Robin Percy MUGUNDHO | VU-BSF-2311-0816-WEE
Derrick AGABA | VU-BSF-2403-1356-EVE
10-FEBRAURY-2026

## Slide 2: Overview
What we’ll cover:
  Problem & Objectives
  System Components
  How It Works (Flow)
  Circuit & Code Highlights
  Demonstration
  Conclusion & Future Work plan
Goal: Show a working single-slot smart parking prototype using Arduino

## Slide 3: Problem Statement And Objectives
Problem
Urban parking chaos time wasted searching, overstaying, inefficient use
Objectives
  Auto-detect vehicle with ultrasonic sensor
  Require button press to confirm and start timer.
  Display status + timer on LCD
  Alert (LED + buzzer) if time exceeds limit (demo: 10s)
  Allow checkout & handle car leaving without button
Benefits: Low-cost, user-intent focused, educational prototype

## Slide 4: System Components
Hardware
  Arduino UNO (brain)
  HC-SR04 Ultrasonic Sensor (distance detection)
  16×2 LCD (status messages)
  Push Button (confirmation/checkout)
  LEDs: Green (free), Yellow (alert), Red (occupied)
  Buzzer (beeps & alerts)
  Breadboard + wires

## Slide 5: Circuit Connections
Key Pins
Ultrasonic: Trig → 9, Echo → 10
LEDs: Green → 2, Yellow → 3, Red → 4
Button → 7 (INPUT_PULLUP)
Buzzer → 8
LCD: RS=12, E=11, D4=5, D5=4, D6=3, D7=2

## Slide 6: Working Principle or Flowchart
States:
  Free → Green LED, “FREE” on LCD
  Car Detected (<15 cm) → Buzzer beep, “Car Detected! Press to Start”
  Confirmed (button press) → Red LED, timer starts, “Slot: OCCUPIED”
  Time exceeded (>10s) → Yellow blink + buzzer pattern, “ALERT! TIME EXCEEDED!”
  Checkout (button) → Reset to free
Flow: Measure distance → Detect? → Button? → Timer → Alert if over → Checkout

## Slide 7: Working Principle or Flowchart

## Slide 8: Key Code Features
Non-blocking with millis() for timer
Button debouncing
Separate flags: carDetected vs slotOccupied
Custom alert: blinkYellowLED() + buzzerAlertPattern()
Distance function with timeout
Full code available in submission

## Slide 9: Demonstration
Tested States
Free: Distance 103.3 cm → “FREE ” (your screenshot)
  Detected: <15 cm → “Press to Start”
  Occupied: Timer running, red LED
  Alert: After 10s → blinking + buzzer
  Checkout: Back to free
Reliable detection, button prevents accidents, alerts noticeable

## Slide 10: Demonstration

## Slide 11: Conclusion
Successfully built a smart parking prototype with:
  Auto-detection + user confirmation
  Timed parking & overtime alert
  Clear feedback (LCD, LEDs, buzzer)
Proves concept for real-world parking aids
Low-cost, easy to build and expand

## Slide 12: Future Improvements
Multiple slots (add more sensors)
Servo gate for auto entry/exit
IoT: ESP8266/ESP32 + app notifications
Real timer (minutes/hours) + billing
Better sensors (IR/camera) for accuracy
Cloud logging like, ThingSpeak)

## Slide 13: Q&A
Questions?
Thank you!